## Slide 1
- made with love by sirbastiano -
Notes: [Sources] - User-provided original presentation slide 1: /mnt/data/SARPyX_project_overview.pptx

## Slide 2
Notes: [Sources] - User-provided original presentation slide 2: /mnt/data/SARPyX_project_overview.pptx

## Slide 3
Notes: [Sources] - User-provided original presentation slide 4: /mnt/data/SARPyX_project_overview.pptx

## Slide 4
Notes: [Sources] - User-provided original presentation slide 5: /mnt/data/SARPyX_project_overview.pptx

## Slide 5
How SARPyX and WORLDSAR fit together
Operational framing for direct CLI use, reproducible execution, and mission-aware preprocessing
OPERATIONAL STACK
Input products
SAFE archives, ZIP bundles, vendor-native SAR products
SARPyX toolkit
unzip · decode · focus · worldsar
CLI + Python API for processing primitives
WORLDSAR repo
Makefile + main.sh + worldsar.py coordinate runtime, tiling, logs, and indexing
Execution outputs
BEAM-DIMAP intermediates, HDF5 tiles, parquet metadata DB, logs
USAGE SPLIT
Use SARPyX directly when the goal is algorithm work
1
You want single-product debugging, notebook-driven experiments, or a narrow CLI chain such as unzip → decode → focus.
2
You need direct control of GPT paths, grid files, Zarr outputs, or custom Python imports from sarpyx.* modules.
3
You are validating one processing stage at a time before freezing an operational recipe.
Use WORLDSAR when the goal is a production-like run
1
You need a stable entry point for local VM and PBS/HPC execution, with explicit mode switching and asset management.
2
You need mission routing, per-swath tiling, cut reports, parquet indexing, and path binding inside the Apptainer runtime.
3
You want the repo to operationalize SARPyX rather than re-implement it. The processing engine stays in SARPyX.
Operationally, the clean mental model is: SARPyX provides the processing primitives; WORLDSAR packages those primitives into a reproducible mission-level execution shell.
Notes: [Sources] - SARPyX overview, architecture, and usage docs: https://github.com/sirbastiano/srp - SARPyX CLI usage examples: https://raw.githubusercontent.com/sirbastiano/srp/main/docs/usage.html - WORLDSAR introduction and execution model: https://sirbastiano.github.io/WORLDSAR/intro.html - WORLDSAR repository (apptainer branch): https://github.com/sirbastiano/WORLDSAR/tree/apptainer

## Slide 6
WORLDSAR apptainer branch: bootstrap and first local run
Minimal sequence for staging dependencies, runtime assets, and a local VM execution
FIRST LOCAL EXECUTION
Repository bootstrap and local run command
git clone https://github.com/sirbastiano/WORLDSAR
cd WORLDSAR
git checkout apptainer
uv sync
make pull-sif
make pull-snap
# optional when product is not already local
make down PRODUCT=<product_name>.SAFE
WORLDSAR_MODE=vm make run \
PRODUCT=<product_name_or_full_path>.SAFE
# equivalent explicit target
WORLDSAR_MODE=vm make run-vm \
PRODUCT=<product_name_or_full_path>.SAFE
1
uv sync installs the Python environment used for helper scripts and support-material download tooling.
2
make pull-sif and make pull-snap stage the SIF container and the .snap userdir expected by the runtime.
3
For local validation, set WORLDSAR_MODE=vm explicitly. The documentation repeatedly recommends choosing the mode on purpose instead of relying on environment defaults.
4
PRODUCT can be a SAFE name under phidown_data or a full path containing a slash. main.sh resolves both cases.
For demos, prefer WORLDSAR_MODE=vm make run-vm first; keep make run for the same recipe once PBS/HPC execution is actually intended.
Notes: [Sources] - WORLDSAR getting started docs: https://sirbastiano.github.io/WORLDSAR/getting-started.html - WORLDSAR runtime assets docs: https://sirbastiano.github.io/WORLDSAR/runtime-assets.html - WORLDSAR input and running docs: https://sirbastiano.github.io/WORLDSAR/input-and-run.html - WORLDSAR repository apptainer branch: https://github.com/sirbastiano/WORLDSAR/tree/apptainer

## Slide 7
RUNTIME ENVIRONMENT
How the apptainer branch turns a PRODUCT argument into tiled, indexed, and logged outputs
ENTRY POINTS
Makefile
Selects vm/hpc mode, stages SIF and .snap, injects runtime env, and dispatches run-vm or qsub.
main.sh
Resolves PRODUCT, validates paths, binds host directories to /work, and forwards GPT and grid settings.
pyscripts/worldsar.py
Infers mission/mode, runs SNAP operators, subsets tiles, validates coverage, and writes parquet metadata.
sarpyx.snapflow.GPT + utils
Operator wrappers plus geospatial helpers used by the mission pipelines inside the container runtime.
Inputs
PRODUCT
GRID_PATH
SNAP_USERDIR
BEAM-DIMAP
Intermediate products
HDF5 tiles
Subset outputs
Parquet DB
Core metadata index
Logs
stdout/stderr or PBS logs
RUNTIME BINDING MODEL
main.sh binds scripts, data, output, cuts, DB, grid, and .snap into /work, then runs python /work/scripts/worldsar.py with /work/data/<PRODUCT_NAME>, the output roots, and the resolved GPT/grid/runtime arguments.
SNAP13
Notes: [Sources] - WORLDSAR repository apptainer branch: https://github.com/sirbastiano/WORLDSAR/tree/apptainer - WORLDSAR raw main.sh (apptainer): https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/main.sh - WORLDSAR raw Makefile (apptainer): https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/Makefile - WORLDSAR raw worldsar.py (apptainer): https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/pyscripts/worldsar.py

## Slide 8
Sentinel-1 acquisition modes drive the router decision
Use the acquisition table as an operational guardrail before selecting the WORLDSAR path
SENTINEL-1 REFERENCE
Mode
Swath / vignette
Nominal single-look resolution
Polarization
Operational reading
SM
80 km swath
slightly better than 5 m × 5 m
single or dual
Stripmap branch
IW
250 km swath
3 sub-swaths (TOPSAR)
5 m × 20 m
single or dual
TOPS branch
EW
400–410 km swath
5 sub-swaths (TOPSAR)
20 m × 40 m
single or dual
TOPS branch
WV
20 km × 20 km vignette
every 100 km
5 m × 5 m
single only
Validate separately
ROUTING LOGIC
SAFE name / manifest token
infer_product_mode(...) inspects S1 mode tokens and path patterns
IW / SM ?
S1STRIP
SM or S1…S6 modes
S1TOPS
IW or EW
The current router explicitly IW to S1TOPS and SM/S1…S6 to S1STRIP. WV is listed in the acquisition tables but not exposed as a dedicated branch, and ambiguous Sentinel names fall back to S1TOPS in infer_product_mode.
Notes: [Sources] - WORLDSAR acquisition modes table: https://sirbastiano.github.io/WORLDSAR/sar-acquisition-modes-tables.html - WORLDSAR raw worldsar.py router logic: https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/pyscripts/worldsar.py

## Slide 9
Sentinel-1 pipeline excerpt from worldsar.py
Repository-faithful excerpt of the Sentinel-1 router and post-chain, reformatted for slide readability
PIPELINE EXCERPT
Sentinel branch (presentation-ready excerpt)
def _sentinel_post_chain(op):
op.ApplyOrbitFile()
op.Calibration(output_complex=True)
op.TopsarDerampDemod()
op.Deburst()
op.do_subaps(...)
op.polarimetric_decomposition(
decomposition="H-Alpha Dual Pol Decomposition",
window_size=5,
)
op.TerrainCorrection(
map_projection='AUTO:42001',
pixel_spacing_in_meter=10.0,
)
if is_TOPS:
for swath in ('IW1', 'IW2', 'IW3'):
sw_op.TopsarSplit(subswath=swath)
results[swath] = _sentinel_post_chain(sw_op)
else:
op.ApplyOrbitFile(); op.Calibration(output_complex=True)
op.do_subaps(...); op.polarimetric_decomposition(...)
op.TerrainCorrection(map_projection='AUTO:42001',
pixel_spacing_in_meter=10.0)
What each step is doing
1
ApplyOrbitFile moves the product onto the refined orbit solution before any calibration or geocoding.
2
Calibration(output_complex=True) preserves complex signal content so phase-aware follow-up steps remain valid.
3
TopsarDerampDemod and Deburst exist only for TOPS data. They remove burst modulation and stitch bursts into a contiguous swath.
4
do_subaps is the SARPyX-specific stage: it creates sub-aperture products for directional diversity, motion sensitivity, and later science metrics.
5
H-Alpha Dual Pol Decomposition converts the calibrated signal into descriptive dual-pol features such as Entropy, Anisotropy, and Alpha.
6
TerrainCorrection projects the result to map space at 10 m pixel spacing, which is what makes grid-based tile cutting straightforward.
TOPS adds TopsarSplit, Deramp/Demod, and Deburst per subswath; STRIP keeps the same orbit → calibration → sub-aperture → decomposition → terrain-correction core without those TOPS-only steps.
Notes: [Sources] - WORLDSAR raw worldsar.py (apptainer branch): https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/pyscripts/worldsar.py - WORLDSAR Sentinel-1 metadata page for observed outputs and processing lineage: https://sirbastiano.github.io/WORLDSAR/sentinel1-metadata.html

## Slide 10
TOPS and STRIP execute differently on purpose
The two Sentinel paths diverge only where the acquisition geometry demands it
EXECUTION GRAPH
TOPS lane (IW / EW)
SAFE input
TopsarSplit
IW1 · IW2 · IW3
ApplyOrbitFile
Calibration
Deramp / Demod
Deburst
Sub-apertures
H-Alpha dual-pol
TerrainCorrection
Per-swath BEAM-DIMAP
outputs
Each subswath is processed independently so tiling can tolerate boundary effects and partial coverage.
Result shape: { IW1: path, IW2: path, IW3: path }
STRIP lane (SM)
SAFE input
ApplyOrbitFile
Calibration
Sub-apertures
H-Alpha dual-pol
decomposition
TerrainCorrection
Single BEAM-DIMAP
output
No split, deramp, or deburst is needed because the input geometry is already strip-oriented.
Result shape: path
Notes: [Sources] - WORLDSAR raw worldsar.py Sentinel routing and pipeline logic: https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/pyscripts/worldsar.py - WORLDSAR acquisition modes table: https://sirbastiano.github.io/WORLDSAR/sar-acquisition-modes-tables.html

## Slide 11
Tiling, coverage validation, and parquet indexing
What happens after preprocessing once the intermediate product exists
POST-PROCESSING FLOW
Product WKT
manifest/CDSE footprint
Grid lookup
check_points_in_polygon
Rectangles
rectanglify
Subset tiles
HDF5 + copy_metadata
Cut report
SUCCESS / FAILURE txt
Parquet DB
metadata[quickinfo]
IMPLEMENTATION NOTES
Geometry and grid selection
If grid_10km.geojson is missing, the script can generate it via python -m sarpyx.utils.grid. Product coverage is intersected with grid points and then inflated into rectangles that become tile footprints.
Actual tile extraction
For non-NISAR products the subset() helper calls SNAP with HDF5 output, output_name=tile_name, geo_region=WKT, and copy_metadata=True. Each successful cut becomes <tile>.h5 in the cuts directory.
TOPS-specific validation logic
TOPS swaths are tiled independently, so some boundary tiles can legitimately fail on a single swath. The aggregate coverage check raises only when the combined TOPS run produces zero tiles at all.
After tile creation, create_tile_database() scans all HDF5 tiles, reads metadata[quickinfo], and writes <tile-folder>_core_metadata.parquet for lightweight cataloging.
Notes: [Sources] - WORLDSAR raw worldsar.py tiling and database helpers: https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/pyscripts/worldsar.py - WORLDSAR Sentinel-1 metadata page for HDF5 tile structure: https://sirbastiano.github.io/WORLDSAR/sentinel1-metadata.html

## Slide 12
Tiling, coverage validation, and parquet indexing
What happens after preprocessing once the intermediate product exists
POST-PROCESSING FLOW
Product WKT
manifest/CDSE footprint
Grid lookup
check_points_in_polygon
Rectangles
rectanglify
Subset tiles
HDF5 + copy_metadata
Cut report
SUCCESS / FAILURE txt
Parquet DB
metadata[quickinfo]
IMPLEMENTATION NOTES
Geometry and grid selection
If grid_10km.geojson is missing, the script can generate it via python -m sarpyx.utils.grid. Product coverage is intersected with grid points and then inflated into rectangles that become tile footprints.
After tile creation, create_tile_database() scans all HDF5 tiles, reads metadata[quickinfo], and writes <tile-folder>_core_metadata.parquet for lightweight cataloging.
Points in polygon
Notes: [Sources] - WORLDSAR raw worldsar.py tiling and database helpers: https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/pyscripts/worldsar.py - WORLDSAR Sentinel-1 metadata page for HDF5 tile structure: https://sirbastiano.github.io/WORLDSAR/sentinel1-metadata.html

## Slide 13
Demo outputs: files, metadata, and lineage
What a successful Sentinel run leaves behind and why those artifacts matter
OUTPUT ARTIFACTS
Filesystem view
OUT/
worldsar_output/
IW1/ ... or <strip>.dim
IW2/ ...
IW3/ ...
tiles/
IW1/<product>/<tile>.h5
IW2/<product>/<tile>.h5
IW3/<product>/<tile>.h5
DB/<product>_core_metadata.parquet
logs/*.stdout.log | *.stderr.log
Representative HDF5 tile content
1
Top-level groups: bands and metadata
2
Bands observed in the docs: Alpha, Anisotropy, Entropy, elevation, localIncidenceAngle
3
Example tile shape in the docs: 1000 × 1127 float32
4
Tile metadata preserves geospatial context and product quickinfo for later indexing.
Lineage captured in metadata
Mission: SENTINEL-1A
Product type: SLC
Acquisition mode: SM
Pass: ASCENDING
Polarizations: VH, VV
Terrain-corrected flag: 1
CRS: WGS84 / Auto UTM
Pixel spacing: 10.0 m range, 10.0 m azimuth
Recorded processing graph in the docs: Apply-Orbit-File → Calibration → Polarimetric-Decomposition → Terrain-Correction → Subset → Write
Notes: [Sources] - WORLDSAR Sentinel-1 metadata documentation: https://sirbastiano.github.io/WORLDSAR/sentinel1-metadata.html - WORLDSAR raw worldsar.py output, subset, and database logic: https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/pyscripts/worldsar.py

## Slide 14
Runtime tuning, monitoring, and deployment sequence
Use local VM mode to prove correctness, then move the unchanged recipe to PBS/HPC
MODE DEFAULTS
Mode
GPT memory
GPT parallelism
GPT timeout
Operational use
vm
64G
16
3600 s
First local validation, low-risk debugging
hpc
128G
164
7200 s
High-throughput cluster runs via PBS/qsub
Monitoring commands + HPC defaults
make status | WORLDSAR_MODE=vm make status | make logs
tail -f logs/*.stdout.log | tail -f logs/*.stderr.log
HPC defaults: queue=cpu_std
select=1:ncpus=192:mem=160g | walltime=22:00:00
DEPLOYMENT ORDER
1
Start with one Sentinel product in SARPyX or WORLDSAR vm mode. Validate the BEAM-DIMAP outputs, tile geometry, and metadata before scaling.
2
Tune only after correctness is proven: GPT memory, GPT parallelism, GPT timeout, grid density, and the exact paths mounted into the container.
3
Move the same recipe to hpc mode once logs are clean and coverage is acceptable. Keep PRODUCT, GRID_PATH, and output semantics identical between modes.
Correctness first in vm, then identical semantics in hpc. Switching mode before stabilizing the product recipe is how you lose traceability.
Notes: [Sources] - WORLDSAR raw Makefile defaults (apptainer branch): https://raw.githubusercontent.com/sirbastiano/WORLDSAR/apptainer/Makefile - WORLDSAR input and running docs: https://sirbastiano.github.io/WORLDSAR/input-and-run.html - WORLDSAR operations docs: https://sirbastiano.github.io/WORLDSAR/operations.html

## Slide 15
Use the tool entry for the right problem
Final decision rule for SARPyX-first experimentation and WORLDSAR-first operations
DECISION MATRIX
Choose SARPyX directly
1
When you want to inspect decode/focus stages independently.
2
When you are tuning algorithms, sub-aperture logic, or custom Python analysis.
3
When you need fast CLI proofs on a small number of products.
4
When you want to import sarpyx.* directly in notebooks, scripts, or workflow managers.
5
When the repo wrapper would add ceremony without increasing repeatability.
Choose WORLDSAR
1
When the run must be reproducible across local VM and cluster environments.
2
When you need standardized tiling, cut reports, metadata DB creation, and run logs.
3
When mission-specific routing and container assets must be part of the interface, not tribal knowledge.
4
When the same command must survive handoff from research to operations.
5
When scale and observability matter more than minimal setup.
Recommendation: validate the Sentinel pipeline with SARPyX on one product, then operationalize the exact same logic in the apptainer branch of WORLDSAR. That sequence preserves technical clarity and avoids scaling unstable assumptions.
Notes: [Sources] - SARPyX usage and architecture docs: https://raw.githubusercontent.com/sirbastiano/srp/main/docs/usage.html - WORLDSAR introduction and running docs: https://sirbastiano.github.io/WORLDSAR/intro.html - WORLDSAR repository apptainer branch: https://github.com/sirbastiano/WORLDSAR/tree/apptainer